## Slide 1
WiFi 6 and 6e In Linux: My Own Experiences. By Bob Primak. For CCS Linux SIG.
May 27, 2025
I moved from Waltham, MA to Lexington, MA. Comcast set me up with new equipment, including an XB7 xFi Comcast Gateway.
I wanted to try out the new WiFi 6 and WPA 3 technologies, partly due to how many neighbors there are here at Brookhaven at Lexington. Our building transmits WiFi and Bluetooth signals readily, making for a crowded 5 GHz spectrum here.
I believe that the best defense in such an environment is to use WiFi channels not used by others, and to have better security than my neighbors.
So there were some hardware changes I determined to make swiftly, to make my online life easier. Or so I thought...

## Slide 2: WiFi 6 and 6e In Linux: My Own Experiences. By Bob Primak. For CCS Linux SIG. May 27, 2025
Hardware change #1: upgrade the Gateway to an XB8. Xfinity XB8 Specs.
https://www.homeowner.com/connectivity/xfinity/xfinity-xb8-review
This gateway can handle WiFi 6, 6e, 5 GHz and 6 GHz with WPA3 encryption. It’s a step up from my supplied XB7 Comcast Gateway, which does support 802.11ax, but not in the 6 GHz band. The XB7 also does not support WPA 3 encryption.
So now I had a gateway without limitations, and which could test whether any new connections were in fact WiFi 6e with WPA 3, and whether the 6 GHz band was being used. In Windows 11 Pro, this feature is turned off by default, and 6 GHz in Linux requires firmware and drivers, which may need to be added, outside of the Linux kernel. Kernels higher than 5.15 do support WPA 3 encryption. But in the Cinnamon Interface, it’s confusing to determine whether or not your connection is using WPA 3. Many Command Line tools are also confusing and don’t give a straight answer.

## Slide 3
Let me show how the Cinnamon Desktop Applet called Network Manager shows (or doesn’t show) the availability of a WPA 3 Personal setting.
(Show the Applet and the two interfaces for setting up or editing a wireless network connection in Mint 22.1.)
WiFi 6 and 6e In Linux: My Own Experiences. By Bob Primak. For CCS Linux SIG. May 27, 2025

## Slide 4
Hardware change #2: Testing revealed that the Qualcomm Atheros WiFi Card which came OEM with my Powerspec Tower PC is not going to be able to do 802.11ax, aka. WiFi 6/6e. It won't do 6 GHz, but it will do WPA 3. So, security-wise, it's a reasonable fallback for Linux if a new WiFi 6/6e card wouldn't work in that OS.
My motherboard in the Tower is the ASUS PRIME H610M-E D4. Specs:
https://www.asus.com/us/motherboards-components/motherboards/prime/prime-h610m-e-d4/techspec/
Its WiFi card fits into a PCIe 3.0 x1 slot.
So how did I know what hardware is inside my PCs? Linux has some commands for that:
(Show Commands and Outputs for identifying WiFi Card hardware.)
WiFi 6 and 6e In Linux: My Own Experiences. By Bob Primak. For CCS Linux SIG. May 27, 2025

## Slide 5: WiFi 6 and 6e In Linux: My Own Experiences. By Bob Primak. For CCS Linux SIG. May 27, 2025
For any WiFi, card or dongle, a good antenna or antennas will be of some help in getting good, solid performance. Also, a network and WiFi environment with fewer and more WiFi-transparent materials. You may need to ID the chipset your WiFi device is using:
(Show Commands for ID of the WiFi chipset in Linux.)
Hardware Info Tools
(Show GUI Tool installation and display.
Pretty useless for IDs.)

## Slide 6
My NUC fared much better. The WiFi Card in there is the Intel Wi-Fi 6 AX201 Gig+. It will do 802.11ax, but only in the 5 GHz band. No WiFi 6e or 6GHz. However, it too does support WPA 3. (A more up to date internal card would be the Intel AX211 card, but the card in a NUC is soldered into place.)
Hardware change #3: I tried changing the WiFi card inside the Powerspec Tower per the instructions from the Micro Center in Cambridge, MA. ASUS (Mediatek) AXE5400 (PCE-AX59BT) card, apparently Revision 2. (Specs and photo:
https://www.asus.com/us/networking-iot-servers/adapters/all-series/pce-axe59bt/
That card did work in LMDE 6 and Mint 22.1, but the connection kept getting broken. Eventually, LMDE 6 stopped workiong at all with Wifi 6, and then Mint stopped working with it. I still don't know what went wrong.
I tried firmware and driver updates, to no avail.
WiFi 6 and 6e In Linux: My Own Experiences. By Bob Primak. For CCS Linux SIG. May 27, 2025

## Slide 7
The Qualcomm Atheros WiFi Card which came OEM with my Powerspec Tower PC:
https://www.ebay.com/itm/335903248606?chn=ps&mkevt=1&mkcid=28&google_free_listing_action=view_item&srsltid=AfmBOooTBpLdz6yxcyrbJDLM19fVeIVo5weMEI9v7d3QRq5NSU5ASVxGWAg&gQT=2
Drivers and firmware updated, but still no longer working under Linux.
I never did figure out what went wrong.
WiFi 6 and 6e In Linux: My Own Experiences. By Bob Primak. For CCS Linux SIG. May 27, 2025

## Slide 8
Hardware change #4: I tried a USB dongle, the Netgear Nighthawk AXE3000, which does do all the WiFi 6 tricks, but needs to occupy a USB slot. Even with an extension cable and cradle (included) this is fine for the Tower with all its spare USB ports (and people laughed at me when I added more USB ports!). But the NUC has only a limited number and really bad locations for USB-A ports. The internal USB 3 port I added has stopped working, at least for the dongle and for flash drives. But I do have one Thunderbolt-3 multi-port USB-A dock, and I decided a different configuration for a dock would be better for saving desktop space.
So that's Hardware Change #5.
(Show on WebCam #2 the NUC configuration for the USB Hub and
Netgear WiFi Dongle)
WiFi 6 and 6e In Linux: My Own Experiences. By Bob Primak. For CCS Linux SIG. May 27, 2025

## Slide 9
Hardware Change #6: I tested the various cards (OEM Qualcomm Atheros, OEM Intel AX201 Gig+, and the dongle). All work well. While LMDE 6 and Mint can't do WiFi 6e (6 GHz) yet (more on Mint and LMDE later), they both could recognize and use the Netgear Nighthawk AXE3000 out of the box, no drivers or firmware needed.
(Show Network Settings and available interfaces now on the
Powerspec for Mint 22.1.)
Hardware Change #7: So the final change I made was to buy a second Netgear dongle, for the NUC, and attach it with the new Thunderbolt dock.
One more nice thing about using a dongle is that it's not a permanent commitment. Any dongle which works with Linux can be used on any hardware which supports its features and throughput rates.
Second Slide Deck: Upcoming changes to Linux Mint and LMDE.
WiFi 6 and 6e In Linux: My Own Experiences. By Bob Primak. For CCS Linux SIG. May 27, 2025